## Bearhawk N57EN
Condition Inspection Checklist

### Condition Inspection Consumables

- Spark Plugs - Autolite UREM40E (if needed)

- ELT batteries – Duracell “D” cell – 6 each

- Oil – Aeroshell 100Plus – 7 qts.

- Oil Sample Kit (Aviation Laboratories)

- ATF fluid for gear struts (if needed)

- Alternator belt - Duralast 15345 (AutoZone) 1.1 cm x 87.5 cm (if needed)

- Air filter replacement element (BA-6108)

- Battery - Odyssey PC680 12 volt (if needed)

- Brake Linings Cleveland 66-105 (8 ea) plus rivets

- Brake fluid Aeroshell #41

- Main Tires -  6.00 x 6 (6 ply or 8 ply) and tubes

- Tailwheel – 8” 2.80x2.50, (4-ply rated tire) and tube

### Firewall Forward

- Fly plane, warm up oil

- Note EIS tach time ___________

- Drain oil

- Send out oil analysis

- Remove spinner

- Inspect spinner for cracks and wear

- Inspect spinner bulkheads for cracks

- Inspect propeller attach hardware and safety wire

- Inspect and clean propeller hub exterior

- Clean propeller blades

- Inspect propeller blades for nicks and cracks

- File/smooth out nicks in propeller blades

- Paint propeller (if necessary)

- Remove engine cowling

- Inspect engine for oil leaks

- Inspect crankcase for cracks and loose bolts

- Inspect cylinders for cracks

- Inspect nose seal

- Remove top plugs

- Differential compression test:

  - #1:		/80

  - #2:		/80

  - #3:		/80

  - #4:		/80

- Check mag timing 25 degrees BTDC

- Check propeller blade track (while top spark plugs removed)

- Clean and inspect top spark plug condition and gap to .016” or replace

- Remove bottom spark plugs

- Clean and inspect bottom spark plugs, gap to .016” or replace

- Rotate bottom plugs to top, and swap left to right sides

- Lubricate spark plug threads and re-install

- Inspect alternator belt for condition and tension

- Inspect starter ring gear teeth

- Remove battery

- Remove air filter

- Inspect airbox for cracks

- Remove and inspect heat SCAT tubing

- Clean air filter with K&N air filter cleaner, let dry

- Clean engine

- Remove heat muffs

- Inspect exhaust for cracks (leaks)

- Inspect engine controls

  - Throttle

  - Mixture

  - Carb heat

- Inspect and re-install heat muffs

- Inspect engine mount for cracks

- Inspect engine mount bushings and bolts

- Inspect firewall

- Inspect oil cooler

- Inspect baffles

- Inspect hoses and fittings

- Inspect brake fluid reservoir, check fluid level

- Torque intake bolts

- Torque exhaust bolts

- Lubricate engine controls with LPS-2

- Lubricate throttle shaft

- Inspect and clean oil screens

- Fill sump with 7 quarts of Aeroshell 100 plus

- Service air filter with K&N air filter oil

- Reinstall air filter

- Have battery tested

- Install new battery (if necessary)

- Run up engine, check for leaks

- Inspect top and bottom cowling and hinges

- Reinstall cowling

### Notes:__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Main Landing Gear

- Inspect tires

- Inspect main landing gear

- Inspect brake lines and calipers

- Remove wheels and tires

- Install new brake linings (if necessary)

- Separate wheel halves, remove all bearing components

- Clean bearing components and inspect for pitting

- Repack wheel bearings with Aeroshell #5

- Reassemble wheels and tires, rotate tires (if necessary)

- Bleed brakes (if necessary)

- Inflate tires to 30 psi

### Tailwheel

- Inspect tailwheel

- Inspect tailwheel fork and spring

- Inspect tailwheel steering link

- Disassemble and clean tailwheel fork

- Inspect condition of rudder lock key

- Clean and repack tailwheel bearings with Aeroshell #5

- Rotate tailwheel (if necessary)

- Inflate to 60 to 70 psi

Notes:__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Right wing

- Check operation of position light

- Check operation of strobe flasher

- Check operation of taxi light

- Remove wing tip

- Remove lower access panels (including tank covers)

- Remove wing lift strut covers (top and bottom)

- Remove wing root fairing

- Inspect wires & connections

- Inspect exterior wing surfaces for cracks

- Inspect wing strut attachment fittings and bolts

- Inspect aileron exterior for cracks, cuts or tears

- Inspect aileron hinge brackets

- Inspect aileron counterweight “pipe”

- Inspect flap exterior for cracks, cuts or tears

- Inspect interior wing structure and interior of skins

- Inspect condition of pushrods

- Inspect bellcrank, turnbuckles, pulleys and cables for play and wear

- Lubricate bellcrank & rod end bearings with LPS-2

- Lubricate aileron hinges with LPS-2

- Inspect flap hinges and lubricate with LPS-2

- Inspect flap return springs

- Lubricate flap pushrod end bearings with LPS-2

- Lubricate flap drive bushings via grease fittings

- Inspect fuel cap, lubricate with EZ-Turn

- Inspect fuel drain

- Inspect fuel tank exterior for leaks

- Inspect fuel lines and fittings

- Inspect fuel quantity sender & wiring

- Inspect front spar

- Inspect wing root area

- Inspect rear spar attach point

- Actuate flaps and inspect through range of travel

- Reinstall wing tip

- Reinstall lower access panels

- Reinstall wing root fairing

Notes:__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

### Left wing

- Check operation of position light

- Check operation of strobe flasher

- Check operation of landing light

- Remove wing tip

- Remove lower access panels (including tank covers)

- Remove wing lift strut covers (top and bottom)

- Remove wing root fairing

- Inspect lighting wires & connections

- Inspect remote compass module and wiring

- Inspect OAT and wiring

- Inspect pitot tube and connections

- Inspect exterior wing surfaces for cracks

- Inspect wing strut attachment fittings and bolts

- Inspect aileron exterior for cracks, cuts or tears

- Inspect aileron hinge brackets

- Inspect aileron counterweight “pipe”

- Inspect flap exterior for cracks, cuts or tears

- Inspect interior wing structure and interior of skins

- Inspect condition of pushrods

- Inspect bellcrank, turnbuckles, pulleys and cables for play and wear

- Lubricate bellcrank & rod end bearings with LPS-2

- Lubricate aileron hinges with LPS-2

- Inspect flap hinges and lubricate with LPS-2

- Inspect flap return springs

- Lubricate flap pushrod end bearings with LPS-2

- Lubricate flap drive bushings via grease fittings

- Inspect fuel cap, lubricate with EZ-Turn (if necessary)

- Inspect fuel drain

- Inspect fuel tank for leaks

- Inspect fuel lines and fittings

- Inspect fuel quantity sender & wiring

- Inspect front spar

- Inspect wing root area

- Inspect rear spar attach point

- Actuate flaps and inspect through range of travel

- Reinstall wing tip

- Reinstall lower access panels

- Reinstall Wing root fairings

### Notes:___________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

### Tailcone and Empennage

- Remove empennage fairings and tail inspection panels

- Inspect longerons, VS and HS attachment points

- Inspect HS brace supports

- Inspect all tailwires for proper tension and thread engagement

- Inspect tail spring mount bolts and weldments

- Lubricate elevator cable ends and trim tab actuatotr with LPS-2

- Lubricate elevator hinges via grease fittings

- Lubricate rudder hinges via grease fittings

- Inspect rudder cable clevis ends and hardware

- Inspect rudder stops

- Inspect exterior of tail surfaces for cracks, cuts and tears

- Inspect elevator counterweights for security

- Inspect trim tab, hinge, pin secured

- Inspect rudder light and elevator trim wiring

- Check operation of elevator trim

- Check operation of tail position light

- Check operation of tail strobe flasher

- Reinstall all covers and gap fairings

Notes:__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Fuselage Exterior

- Inspect exterior skins for cracks, cuts and tears

- Inspect static ports

- Clean & inspect belly

- Remove gear leg fairings

- Remove bottom skin between landing gear legs

- Disassemble, clean and inspect gascolator

- Inspect fuel lines for any wear or chaffing

- Inspect all wiring under floor pans

- Inspect brake lines for leaks or chaffing

- Inspect landing gear and all attachments

- Inspect external antennas

- Inspect condition of rear windows

- Inspect door skins for cracks or loose rivets

- Inspect and lubricate all door hinges and latches

- Inspect front side windows for cracks or crazing

- Inspect windshield for cracks or crazing

- Inspect boot cowl

### Notes:___________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

### Fuselage Interior

- Remove front and rear seats

- Inspect seats, seat mounts and slide tracks

- Remove center floor panels

- Remove front floor panels

- Remove covers in ceiling

- Remove rear baggage bulkhead

- Inspect fuselage aft of baggage compartment

- Inspect static port hoses and connections

- Inspect and lubricate rudder and brake pedal assembly

- Inspect brake lines and rudder cable connections

- Inspect control stick assembly and lubricate

- Inspect and lubricate elevator bellcrank assembly

- Inspect both gang pulleys

- Inspect flap cables, pulleys and turnbuckles

- Inspect and lubricate flap handle assembly

- Check landing gear strut fluid levels (fill with ATF as needed)

- Inspect ELT mount

- Replace ELT batteries (if necessary)

- Test ELT with radio tuned to 121.5 (5 minutes past the hour)

- Inspect strobe power supply

- Inspect trim and flap relays and wiring

- Inspect antenna connections

- Inspect all seat belts

- Inspect parking brake and cable

- Inspect instruments, avionics, and wiring

- Inspect manifold pressure tubing

- Inspect firewall and forward fuselage structure

- Reinstall all cover panels

- Reinstall floor cover panels, seats, and rear baggage bulkhead

- Reinstall exterior skins and covers

Notes:__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Make notation in aircraft logbook(s).

This condition inspection was completed on  ________/________/_________

_________________________________________________________________
Printed Name

__________________________________________________________________
Signature  and Certificate Number